## Slide 1: AI and ML based trash collecting boat/bot: Manual and Auto Mode
Group 1:
    Sumedh Kamat
    Snehal Vasanakar
    Prasanna Gramopadhye
    Akshay Gaikwad
    Project Guide:- Prof. Mrs. Radha A. Ranjekar, Assistant professor
    Electrical Department, PVG’s College of Engineering, Pune

## Slide 2
Problem Statement
Water pollution with floating garbage is getting more and more serious in many countries causing a major environmental problem that endangers the lives of river inhabitants.
Contemporaneous methods find it difficult to manage the volume of solid waste generated by the growing urban population.

## Slide 3: Proposed System
Proposed system is an unmanned water trash collector boat, which will collect floating garbage inside it.
There are 2 modes of operation for this boat
  Manual control mode
  Automated control mode
Trash gets accumulated inside boat in flow when it reaches to the trash.

## Slide 4: Workflow
Video streamline captured by camera, is sent to rasp-pi for processing of video frames at 30 FPS rate
Rasp-pi then uses a pretrained model of trash on each frame to compute object detection in the background (It detects if there is any trash in that frame)
If it finds any, draws a bounding box around that detection on that particular frame.
Results then are sent to the moderator’s screen for further controlling in manual mode and in case of automation mode, processor computes it’s actions accordingly on it’s own.

## Slide 5: Trash boat navigation and Waste Collection
Once we detect the targeted trash, commands are given to boat via wifi (VNC) using laptop/suitable controller.
Instantaneous actions are provided to boat motors via raspberry pi to navigate towards the trash (by controlling person in manual mode or by automation)
Once the boat is completely filled with trash, it is then driven to nearest station for unloading of trash.

## Slide 6: Block Diagram

## Slide 7: Literature review
A US based company ‘Wasteshark’ has already achieved a manually driven trash collector boat, our main aim will be to maximize the efficiency of boat and provide a way cheaper option for it.
Reference Links:
https://youtu.be/dBA0-W4E0Gk https://youtu.be/f9Y2yFj0890

## Slide 8: Proposed Design
Approximate dimensions :
L:B:H = 3.5 : 2.2 : 2.4 (in feet)

## Slide 9: Dependencies and Challenges
Controlling of boat would be a challenge in high current water flow, especially in the rainy days when the water flow of drainage system is high.
Range for communication between user and system can be problematic.
Project has major dependency on the controller being used for speed, accuracy and water resistant behavior aka physical properties.
Unsupervised learning model dependencies are quite vulnerable to our boat as it can not differentiate untrained variables such as rocks,etc.

## Slide 10: Results on Trash Detection
Above image shows the successful detection of plastic waste on our custom trained model (Numbers denote confidence level)

## Slide 11: Images of model : Right side View

## Slide 12: Images of model : Left side View

## Slide 13: Images of model : Front View

## Slide 14: Images of model : Backside View

## Slide 15: Final results 1: Manual Mode

## Slide 16: Final results 2: Manual Mode

## Slide 17: Final results 3: Manual Mode

## Slide 18: Final results 1: Auto Mode

## Slide 19: Final results 2: Auto Mode

## Slide 20: Final results 3: Auto Mode

## Slide 21: References
1) Computer Vision and Pattern Recognition using YOLO algorithm : https://arxiv.org/abs/1506.02640
2) Artificial Intelligence Enabled Robotic Trash Boat to Drive and Harvest Floating Trash from Urban Drain by P.Elavarasi, S.A.Meenuppriya, M.Monira, P.Priya, P.Reni. Department of ECESRM TRP Engineering College, Trichy, TamilNadu, India.
3) Raspberry pi controller & sensors : https://tutorials-raspberrypi.com/raspberry-pi-sensors-overview-50-importantcomponents/#wireless
4) Yolo Research paper and Information: https://github.com/pjreddie/darknet

## Slide 22: Thank you!

## Slide 23: Auto Mode Algo 1: Nearest Trash detection

## Slide 24: Auto Mode Algo 2: Turning Instructions